## Slide 1: Data-Driven Approach to Variational Synthesis of Mechanisms
Shrinath Deshpande

## Slide 3
Problem
Task for
Synthesis
Solution
Design
Prototype
Machine Design Process
Mechanism Design

## Slide 4: Motion Generation : Classical Burmester Problem

## Slide 5: Path Generation

## Slide 6: Mechanism Design
Task of Moving Hip
From Sit to Stand
In Natural Motion
Representation
Suitable for Solvers
Requires Understanding
the task and solver needs
Computational Solver
Problem Solving
Problem Setup

## Slide 7: Mechanism Design
Active topic in research since past 4 decades
Discovery of various geometric and computational methods
Focus was on theoretical aspects of the problem prevalent in Academic Setting
Available tools require expert user to get useful results

## Slide 8: Reasons for Unavailability of Commercial Tools
Susceptible Synthesis Solvers
    Chaotic System : due to highly nonlinear nature of the inverse problem
Design Experience
    Research community did not consider needs of a non-expert user
    Inability of capturing designer’s intent in problem setup yields misfit solutions

## Slide 9: Mechanism Design
Task of Moving Hip
From Sit to Stand
In Natural Motion
Representation
Suitable for Solvers
Requires Understanding
the task and solver needs
Computational Solver
Most Prior Research
Focused on
Critical in Practice
Precision Points
Fourier Curve Fitting*
Geometric Constraints
Global Optimization
  Genetic
  Sim. Annealing
  PSO
Homotopy
Algebraic Fitting

## Slide 10: Synthesis Frameworks
Computational Efficiency
Overall
Effectiveness
(Robust
Prolificacy,
Practical
Considerations,
Useful Solutions)
Desired Region
FD Based
Path Generation
Algebraic Fitting for
Classical Burmester
Problem
1
2
2 = Clustered Database
Query Approach (JCISE’19)
1 = Extended Burmester
Problem (JMR’17)
3
3 = AI Assistant
IDETC 19
(Submitted to JMD’19)
Genetic
Algorithms
Homotopy
Methods

## Slide 11: Proposed Framework
High Level Input
and
Interactive High Level Control
Solution Concepts, Input Suggestions
AI Assistant
User Interface
User Input
Refined Variational
Input
S1
Outputs
Synthesis
Solvers
Input Recognition, Imputation, and
Type Synthesis
Solution Clustering
Output
S2
Sn
.
.
.

## Slide 12: Understanding Solver Requirements and Limitations
Susceptible to Input Data ( Garbage in -> Solver -> Garbage out )
    Input Data Conditioning
Needs Specific Set of Information
    Missing Input Imputation
Prolificacy vs Accuracy
    Variational Synthesis
Mathematical Limitations in Specifying objectives

## Slide 13: Incorporating User Intentions
Capturing Robust Features from User Inputs
    Input Denoising and Recognition
Finding their projections on manifold of plausible inputs space
Provide a handle to control the entire process
Providing feedback

## Slide 14: Deliverables of a Concept Generator
Computational Creativity
Quantity beats Quality ?
Insight about the problem
    How likely it is to find good solutions for this input?
Higher Level Assessment Task and Obtained Solutions
    knowledge base that learns the connection of task and obtained solutions

## Slide 15: Motion Generation : Classical Burmester Problem

## Slide 16: Motion Generation
Small Change in Input Renders Practically Useless Solution

## Slide 17: Precision Position vs Designer’s Intent
Notes: Notion of Continuity is lost

## Slide 18: Limitations of Precision Position Approach
Loss of Continuity Information => Defects in Linkage
Restrictive Objective
    Mathematically Optimal Solution may not be practically optimal
    discards a large proportion of numerically sub-optimal solutions with desirable properties

## Slide 19: Path Generation

## Slide 20: Limitations of Fourier Descriptor Approach
Only Defined for Four-Bar with Revolute Joints
Restrictive Objective
    Mathematically Optimal Solution may not be practically optimal
    discards a large proportion of numerically sub-optimal solutions with desirable properties

## Slide 21: Need of Generative Model
Input Conditioning and Imputation requires capturing the underlying pattern
Learning joint probability distribution of linkage parameters
Generate Variational Inputs to exploit nonlinear nature of the problem

## Slide 22: Variational Input
Common Approach is to change the input randomly within a tolerance range
  Combinatorial Optimization (NP Hard)
Informed Modifications on Input
  Requires knowledge about the properties of coupler motions (or paths) of planar linkages.

## Slide 23: Variational Synthesis
Finding Solutions to Variational Input, Post processing of outputs to gather distinct solution concepts
Each concept is probability distribution of linkage parameters that pertain to same family of mechanisms

## Slide 24: Generative Model
Variational Auto Encoder (VAE) and Conditional VAE (C-VAE)
Number of parameters significantly smaller than the amount of data we train them on
Models are forced to discover and efficiently internalize the essence of the data in order to generate it.
– Richard Feynman
“What I cannot create, I do not understand.”

## Slide 25: Representation Learning of Linkage Trajectories
Learn Salient Features of Linkage Trajectories
Given an unknown trajectory, recognize the potential linkage type.
Six-Bar Linkage
Four-R Linkage
Slider Crank Linkage

## Slide 26
X can be Coupler Trajectories or Entire Linkage
X is Generated by a Natural Process, involving an unobserved continuous hidden variable z

## Slide 27: VAE
Observed data is supposedly generated by an unknown function of continuous latent variables
We would like to infer these salient attributes z based on observed X,
Recognition Model approximates
Intractable

## Slide 28: VAE
z is assumed to have a prior probability distribution
The training loss for VAE becomes,
Training Objective :

## Slide 29: Input Recognition and Preconditioning

## Slide 30: Motion Characterization in Latent Feature Space : Type Synthesis
Latent Embeddings of coupler motions sampled from random Fourbar, Sixbar and Slider Crank linkages
Notes: Here, we can see that points clouds are overlapping. This overlapping concurs with the kinematic theory which says that some motions can be obtained from all of the overlapped mechanism types.
(This also is a good indicator that the learned latent space is in sync with the kinematic theory.)
I am stating this because people may think that good latent space embedding is the one where the data is separated.

## Slide 31: Paths Corresponding to Latent Embedding

## Slide 32: Variational Synthesis
Notes: Preconditioning of the Input for Susceptible Solvers

## Slide 33: Linkage as Observed Variable (X)

## Slide 34: C-VAE
Observed data is supposedly generated by an unknown function G of continuous latent variables and a condition Y
Recognition Model approximates
C-VAE learns to model the conditional distribution of X and Y

## Slide 37: Designs for Gait Rehabilitation Device

## Slide 38: Database Generation
Performance of ML based approaches highly depend on the dataset on which they are trained on
Balanced Data
Diverse Data Samples
Normalized Data

## Slide 39: Database Generation Curiosity Driven Exploration
State : Mechanism State
Action : Change in Linkage Parameters
Reward Model : Auto Encoder Reconstruction Loss
Encoder
Decoder
Reward for reaching State

## Slide 40: Database Generation with Curiosity Driven Exploration
Deep Deterministic Policy Gradients (DDPG)

## Slide 41: DDPG
Actor tries to approximate the best policy which maps a state to optimal action
Critic tries to approximate the predict the correct Q value
Critic is trained to Satisfy Bellman Equation
Actor is trained by policy gradients given by,

## Slide 42: Things to Note
Synthesis Algorithms are combined with Deep Learning
    To intelligently manage uncertainties and provide highly accurate distinct design solutions
A novel idea of an ML intermediary was introduced, which communicates between the user and computational algorithms.
  Intelligently captures the user’s intention while managing the input for synthesis algorithms.
  Interprets numerous solutions returned by the solver and provides the user with a distinct distribution of concept solutions.

## Slide 43: Things to Note
This approach derives from the existing kinematic knowledge to create a new framework for mechanism synthesis
Solves problems that have had no good theoretical underpinning, such as defect-free generation, conditioning of the input, and contextual concept generation.
Deep learning was used to learn the meaningful representations of linkage parameters and used in a novel way to enhance the users’ design experience.

## Slide 44: Next Steps
Data Representation
Domain
Architectural
Image Based Approach
Consistent data format for all planar mechanisms
Intuitive approach to apply constraints
Benefits of Data Bucketing
Leverage Established Deep Learning Architectures
GANs
Better Reconstruction Quality for Images
Attribute Vectors
Better Manipulation of Inputs
Attribute Vectors
Better Manipulation of Inputs
MultiDOF
Type Synthesis
Workspace Specification
Spatial Mechanisms
Scaling the approach in three dimensions

## Slide 45: Image Based Approach
2D Array of Discretized Information
Specify Information in an Intuitive Way
lets you apply constraints which are hard to specify mathematically consistent manner
  Ex. Restriction on Swept Volume

## Slide 46: Image Based Approach
k-Channel Image
Each channel contains one aspect of information
Established Architectures like Generative Visual Manipulation can be used to perform Interactive Mechanism Design

## Slide 47: Generative Manipulation on the Mechanism Image Manifold

## Slide 48: Generative Manipulation on the Mechanism Image Manifold
Find Feature Vectors z, Based on User Input Recognition
Additional constraints can be used for local search in z space with following objective :
argmin
Distance from
Pixelwise Constraint Loss
Discriminator Loss

## Slide 49: path-VEA Preliminary Results
Denoising + Inpainting
Shape Transformation

## Slide 50: 3D Images
Images can be stacked during entire simulation to form a 3D image containing rich information about mechanism
Interesting spatial and temporal patterns can be obtained
    Timing related patterns (ex. Quick Return) for higher order linkages

## Slide 51: Acknowledgment
A Computational Framework for Data-Driven Mechanism Design Innovation
(CMMI-1563413)

## Slide 52: Extended Burmester Problems
No Solution

## Slide 53: Extended Burmester Problem
Given n geometric constraints, determine the type and dimensions of all planar four-bar linkages consisting of revolute or prismatic joints.
Geometric Constraints can be on poses or pivots or something equivalent.
Geometric Constraints can be linear, non-linear, exact or approximate.
Includes finding answers to Burmester problem for which a solution may not exist.

## Slide 54
Finding a point that lies on Circle or Line

## Slide 55: Review: Unified Representation of Dyad Constraints
A unified treatment of the geometric constraints of the building blocks (dyads for four-bar) of mechanisms
Homogeneous Representation of Line and Circle
when

## Slide 56: Planar-Quaternions and -Kinematic Mapping
Review: Image Space Approach

## Slide 57: Constraints on Homogeneous Form
Above is defined by a set of 8 homogeneous coordinates (p1...p8)
However, there are only 5 independent mechanism parameters related by
There are two quadratic conditions on (p1...p8)

## Slide 58: Geometric Constraints on Planar Mechanisms
Pose Constraint on Coupler

## Slide 59: Geometric Constraints on Planar Mechanisms
Point Constraints on Fixed Pivots
Point Constraints on Moving Pivots

## Slide 60: Geometric Constraints on Planar Mechanisms
Curve Constraints on Fixed Pivots
  When
  When

## Slide 61: Linear Constraints in the Coefficient Space
Unified Form

## Slide 62: Algebraic Fitting of Linear Constraints
We form a system of linear equations given by,
Singular Value Decomposition [A] = [U][S][V]T
Null space formed by right singular vectors corresponding to zero singular value is the solution space for optimization given by

## Slide 63: Constraints in the Null Space
Candidate solution vector
Unified Linear Form
Substitute p in the unified form of linear constraints
Substitute p in the non-linear constraint
To get

## Slide 64: Constraints in the Null Space
Two quadratic Conditions
In the null space

## Slide 65: Optimal Model
Minimize
where
while g is an inequality constraint.
Objective function represents algebraic fitting error of relaxed geometric constraints.

## Slide 66: Minimization using Lagrange Multipliers
Lagrange Objective function is formed,
Taking partial derivative we form the system of polynomial equations given by,

## Slide 67: Example : Landing Gear
Synthesize a four-bar linkage such that,
Mechanism passes through precision poses 1-2-4-5
Closely Approximates third pose
Fixed pivots desired to lie on or inside the allowed region.

## Slide 68: Progressive Relaxation of Constraints
Five position synthesis to see if exact and useful solution exists
Relax third position and minimize its error function and check for useful solutions.
Add non-linear inequality constraint for circle

## Slide 69: Solutions for Relaxed Third Pose
Six dyads obtained which in combination make up to 15 linkages.

## Slide 70: Strict Circle Constraint
Three dyads with fixed pivots exactly on desired circle are obtained.
First Mechanism is Grashof crank-rocker Mechanism

## Slide 71: Minimization with Inequality Constraint
Four dyads are obtained as a solution for minimization problem with inequality constraint.

## Slide 72: Database Query Approach for Defect Free Linkage Synthesis
Notes: Signature should be
1) invariant to similarity transformations
2) Capture the information related to shape of motion
3) Facilitate partial matching