## Slide 1: Mechanism Synthesis
A Data Driven Approach

## Slide 2: Motion Generation
  Task is to synthesize a planar linkage,
  which produces a desired planar motion
  without dis-assembly .
  Linkage might also have to satisfy
  some other constraints

## Slide 3: Unsolved Problems in Kinematic Synthesis
Defects in Mechanism
  Branch Defect
  Circuit Defect
  Order Defect

## Slide 4: Tools required for Synthesis
Incorporation of Practical Constraints
  Region Constraints for pivots
  Obstacle Avoidance
  Torque-Velocity Constraints
Tool having a dialogue with mechanism designer
  An interactive tool which user can tinker with to get his job done
  Tool should provide visualization of process that is being carried out
Variational Synthesis

## Slide 5: Our Prior Work…
N-Constraint Motion Generation with minimum algebraic fitting error. Presently no consideration is given to find defect free linkage.
Regional constraints can be modeled and linkage with minimum fitting error can be found.
Real-time solution for the above said problems

## Slide 6: Problems with Task Formulation
Finite Position Synthesis inherently ignores continuity requirement of coupler curve
Precision Pose constraint is an accuracy overkill for specifying a motion
  Sometimes user needs is a higher-level general sense of motion instead of precise interpolation at particular points.
  N-pose least square synthesis also suffers from this formulation

## Slide 7: Atlas/ Catalogue/ Database Approach
Pros:
Always finds defect free mechanism
Comes up with many concept solutions
Can be generalized to give any type of linkage
Cons:
Not a standalone method, (requires server with database)
Subsequent Optimization for fine tuning is needed

## Slide 8: Literature Review
Ullah and Kota[1]:
Method for shape comparison of closed planar curves.
  Cumulative Angular Deviant function which is independent of scale, rotation, and translation
  The function is represented as Fourier series. (First 20 harmonics)
It is used as objective function in path synthesis via optimization.

## Slide 9: Literature Review
Huafeng Ding et. al[2]:
Synthesis of the whole family of planar 1-DOF kinematic chains and creation of their atlas database
An atlas database of 1-DOF kinematic chains with 6–14 links is established.
The atlas database contains all the valid topological graphs classified by their structural characteristics. Once topology is selected, the dimensions are calculated by some other methods.

## Slide 10: Literature Review
Jinkui Chu et. al[3]:
Dimension Synthesis of Spatial Four-Bar Linkage Through Numerical Atlas Method
Atlas for Function Synthesis and Path Synthesis is created

## Slide 11: Literature Review
Constraint-Based Design & Optimization Group (CBDO), Mechanical Engineering, University of Bath:
Specify the required output path
Use the catalogues to find a suitable candidate mechanism
Additional constraints can then be imposed and constraint modelling software used to adapt the selected mechanism to meet these.

## Slide 12: Literature Review
Atlas based Methods are developed only for Close Path Synthesis
Possible Reasons
closed loop paths were the important ones
  But, Open paths and motions gaining increasing importance with advent of Modern technologies like nanotechnology or bio-mechatronics,
  complex spatial and coupled movements or mechanisms for miniature and micro assemblies
Its easier; don’t have to deal with partial matching (part-to-whole)

## Slide 13: Algorithm
Build a database of trajectories generated by a uniform distribution of four-bar linkages in its parameters space.
  Parameter space is chosen such that mechanism has realistic dimensions and all shapes of coupler curves can be generated.
  Store Compact Invariant Representation of trajectories
For a given trajectory find the set of close trajectories from database.
  Clustering of Trajectories
Find the set of mechanisms corresponding to such trajectories.

## Slide 14: Clustering of Trajectories
Trajectory is a series of discrete poses
  High Dimensional (for 60 poses = 60x3 = 180 numbers)
Naïve Clustering suffers from curse of dimensionality
Need compact and tolerant representation of Four-bar Trajectories
  Auto-Encoders
Clustering in the reduced space is easy!

## Slide 15: Auto-Encoders : Training
BottleNeck
Minimum
Neurons
Possible
Input
Reconstructed
Input
Encoder
Decoder
[5]
[150]
[150]
[180]
[50]

## Slide 16: Training Data
Total 200,000 Trajectories
  Each trajectory is a set of 60 poses
  Dim of each trajectory => [60, 3] flattened to [180]
For cross validation, training and test trajectories are randomly divided into 160:40 split
  Error results are same for each such runs.

## Slide 17: Implementation Details
Different Number of Bottle-Neck Neurons are tried out
Best fit with compact Neuron layer : # neurons = 5
Each trajectory is reconstructed by using its 5 dim z_feature
10 Trajectories along with their reconstructions

## Slide 18: Auto-Encoders : Encoding -> Clustering
BottleNeck
Z Features
(a Compact
Representation
Sufficient for
Reconstruction of
Input)
Input
Encoder
Clustering

## Slide 19: Clustering
DBSCAN
  Finds core samples of high density
  expands clusters from them
  Estimated number of clusters for: 5-dimesion case = 183

## Slide 20: Some Interesting clusters

## Slide 21: Some Interesting clusters

## Slide 22: Different Mechanisms With Similar Motion

## Slide 23: Trajectory Signatures
Motion of the coupler is divided into path and angle.
Compute the invariant signatures of Path first
Couple the signature with orientation.

## Slide 24: Path Signature
Fit piecewise cubic B-splines to target path.

## Slide 25: Path Signature
Fit piecewise cubic B-splines to target path.
Compute,
Where,
Calculate, cumulative Integral

## Slide 26: Invariant Representation of motin

## Slide 27: Orientation Prediction
Coupled information of path and orientation
Database can be used to learn this sequential information
Analogous to Text prediction and completion implemented in Cell-Phones
Quick Real-Time feedback by onboard computation

## Slide 28: Sequence Learning for coupler orientation
LSTM
RNN
Path Sequence
Orientation Sequence